## Slide 1
An integrated interpretation of logging and 4 acid digest ICP-MS geochemistry.
Example from a porphyry copper system.
International Applied Geochemistry Symposium 2024
Workshop
Applied Geochemistry of Porphyry Copper Deposits.
Scott Halley
SUNDAY OCT 13, 2024

## Slide 2
This exercise contains assays and drill logs from a cross section through a porphyry Cu system.
The exercise is partly about learning some of the functions in ioGAS, but mostly about learning how to interpret 4 acid digest ICP geochemical analyses.
It is set out as a workflow for creating an interpretation of the data based on merging the logging information and assay data.
This is a real-world example, warts and all.
Logging information is missing from some holes, so we will use geochemistry to fill in the blanks.
Create a series of geochemistry plots from the assay data. Colour the points by the logging codes. Unlogged intervals will have a default colour.
Identify “clusters” in the data, ie groups of points with a high degree of geochemical similarity.
See if the logged rock types match the clusters in the data.
Re-code the points according to the chemistry to obtain a best fit between observations (logging) and measurements (assays) and assign the unlogged data to the correct groups.
The compositions of the rock are a result of geological (magmatic) processes. Identify what those processes were.

## Slide 3
Open the provided file

## Slide 4
Make sure East, North, Elevation values are set, and the correct elements_units are assigned; ie green dots next to the elements .

## Slide 5
In the Select Variables dialogue box, use the green arrow to select all elements. Then click OK.

## Slide 6
Go to Data, Data Doctor to see if there are any QAQC issues. If there are, the issues can be resolved here.

## Slide 7
Check the spatial context of the data. Go to Home, Attribute Map 3D. This is a cross section of drill holes through a porphyry Cu deposit.

## Slide 8
Check the context of the assay data. Go to Home, Attribute Manager. In the bottom left corner of the attribute manager, use the drop-down arrow to select Cu as the plotting variable. Select 10 equal bins and a linear colour stretch. Auto-Attribute. Now on the cross section, the center of the porphyry system will be quite apparent.

## Slide 9
Use immobile trace elements to chemically classify the data points.
Which trace elements are immobile?

## Slide 10
Create the following set of plots;
Sc vs Ti, Th, V, Y, Nb, P (ioGAS xY plots)
Ti vs Sc, Th, V, Y, Nb, P (ioGAS xY plots)
Sr/Y vs Y (this is an ioGAS Diagram)
V/Sc vs Sc (need to calculate a ratio to create this plot)
Jensen Cation plot (this is an ioGAS Diagram)
Sc vs Cr, Ni (ioGAS xY plots)
Note, Zr and Hf will not be used in this process since zircons are usually poorly dissolved with a 4 acid digest.

## Slide 11
Calculations can be done in excel before you import a file, but they are easily done inside ioGAS.
On the top tool ribbon, go to Calculation, New Calculation.
In this case, I have selected V_ppm and Sc_ppm as the variables to use in the calculation.

## Slide 12
Creating Diagrams. Select the plotting variables you would like to use. In this case, I chose V/Sc and Sc. On the top tool ribbon, go to Diagram, New Diagram, New XY Diagram. Click on edit diagram to add a suitable heading, fix and label the axes, etc, then save the diagram for future use.

## Slide 13
If you are likely to use the same suite of geochemistry plots on a regular basis, then it is a good idea to Save a Template.
On the top tool ribbon, go to Home, Save Template.
Next time you open a file, instead of recreating all the usual plots, you can go to Home, Open, Open Template, User. The suite of plots you created will come up on the User list

## Slide 14
Why plot Scandium?
Tholeiites plot on an Fe-enrichment trend; enriched in Scandium.
Calc-alkaline rocks trend to lower Fe; depleted in Scandium.
Tholeiitic Trend
Tholeiitic Trend
Calc-Alkaline Trend
Calc-Alkaline Trend
Notes: In tholeiitic melts, Fe olivines and Fe pyroxenes in the source region are the first minerals to melt. On the cooling cycle, Fe pyroxene is the last phase to crystalize. Tholeiites are described as a magma series showing Fe-enrichment, but that signature is accentuated if we plot Sc instead.
In high pressure, hydrous environments, hornblende is stable in the source region. Hbl is a repository for Sc. Therefore calc-alkaline rocks are relatively depleted in Sc. For this reason, Sc vs SiO2 (or Zr, Th, Nb, etc) shows a step displacement between Fe-rich tholeiites and the most mafic of the calc-alkaline andesites.

## Slide 15
In the Attribute Manager, Load the provided attribute Legend file

## Slide 16
In the Attribute Manager, select Rock_Name, auto-attribute, use existing legend.

## Slide 17
Sc vs Ti, Th, V, Y, Nb, P. What clusters can you recognize in the data?
Greens are mafic, yellow Th-rich, V-poor felsic, red-pink is porphyry, grey, cyan logged as sediment. Areas of mixed colours are likely due to mislogged rocks. Note; with the chemistry, we can pick compositional groups, but not rock types ie can’t see textures. Fragmental rocks will be assigned to groups based on the dominant clast provenance.

## Slide 18
Sc vs Ti, Th, V, Y, Nb, P. Add a point density contour overlay. Look for clusters in the data.

## Slide 19
Ti vs Sc, Th, V, Y, Nb, P. What clusters can you recognize in the data?
Greens are mafic, yellow Th-rich, V-poor felsic, red-pink is porphyry, grey, cyan logged as sediment. Areas of mixed colours are likely due to mislogged rocks. Note; with the chemistry, we can pick compositional groups, but not rock types ie can’t see textures. Fragmental rocks will be assigned to groups based on the dominant clast provenance.

## Slide 24
Now start coding assays that have no logging and recode samples that appear to be incorrectly logged. Start with groups that are very obvious and work down to things that are more ambiguous.
There is a subset of the mafic rocks that have unusually high phosphorous. Assign these first. Use the Ti vs P plot. Create a new colour group called Mafic high P.
Assign the relevant points to this group. Once you have created this group, turn them off using the Visible tick box in the Attribute Manager so that they are removed from other plots and not overwritten.

## Slide 25
Next, create a group called Mafic Volcanics to capture unlogged or mis-logged samples into the Mafic group.
Select these from a plot of Ti vs Nb.

## Slide 26
Next, create a group called Mafic high Ni.
Select these from a plot of Sc vs Ni.
Turn off the Mafic and Mafic high Ni groups using the Visible tick box in the Attribute Manager so that they are removed from other plots and not overwritten.
Delete the original Mafic Volcanic Flow group. The few remaining points in this group will revert to the default colour

## Slide 27
Next, separate out the rhyolitic rocks. These are most obvious on Ti vs Th, Nb plots.
The Rhyolite Basement has distinctly higher Th and Nb. There is another unit logged as Magmatic Hydrothermal Injection Breccia which also has high Th and Nb and seemingly has chemical affinities with the Rhyolite Basement. These rocks plot with quite a scatter rather than as tight groups, consistent with fragmental rather than coherent facies rocks.

## Slide 28
Create a new colour group called Rhyolite. Select the points from the Ti vs Th plot. See where they plot on the bivariate plots. Delete the original Rhyolite Basement and Magmatic Hydrothermal Injection Breccia groups.

## Slide 29
Now look at the V/Sc vs Sc plot. Felsic magmas with high contents of high field strength elements are commonly generated during mid-crustal melting under conditions where magnetite crystallizes early and fractionates. Create a new colour group called Rhyolite Basement. Make it blue. Select those “Rhyolite” points that have a low V/Sc ratio.

## Slide 30
Turn off the Rhyolite Basement group. Go back to the Ti vs Th, Nb plots. Note that the rhyolites are bimodal in the Th content. Make a new colur group. Make it orange. Add the high Th rhyolites to this group.

## Slide 31
The remaining points now include various porphyries and the sediments/conglomerates. The sediments and conglomerates are distinctly different to the porphyries on a Sc vs Ti plot. Retain the Epiclastic conglomerate unit as it is logged, and add the extra high Sc-Ti data to the Sedimentary Unit.

## Slide 32
The remaining points are various porphyries or porphyry-clast breccias.
There are some obvious subsets here. There is a very coherent high Ti-Sc-Nb porphyry, and a strange low Y group.

## Slide 33
Make a new colour group. Name it Porphyry low Y.
Select the low Y cluster from the Ti vs Y plot.

## Slide 34
Make a new colour group. Name it Porphyry low Y.
Select the low Y cluster from the Ti vs Y plot.

## Slide 35
Make a new colour group. Name it PreMineral Sill. Select the data cluster with high Ti values relative to other porphyries.
If you then delete the old PreMineral Sill colour group, any of these rocks that were mis-logged will revert to the default colour group.

## Slide 36
The remaining data points are mostly logged as Intermineral Monzodiorite and Intermineral Crowded 2 Hb-Bt, but have significant overlaps.
Rather than looking at binary plots, pick 3 elements that show a degree of separation and make a ternary plot.
I chose Nb-Sc-Th.

## Slide 37
Use the Nb-Sc-Th. Ternary plot to reclassify all of the remaining points to either the Intermineral Monzodiorite or Intermineral Crowded 2 Hb-Bt.

## Slide 38
Here is the final section, which is a synthesis of both the chemistry and logging.
We could change the symbol shape for samples logged as breccias.
You can see runs of samples where the colours are mixed. These are zones where the chemistry is ambiguous. Some degree of manual overwriting is still required.

## Slide 39
Once we have finished this initial part of the interpretation, go to Data on the top tool ribbon, Make Variable, From Colour. Enter the name of the new variable as “Composition”. Save the file.

## Slide 40
Now, if you go to Data on the top tool ribbon, then click on the Data icon, ioGAS opens a window showing the data table. On the far right of the table, there will be a column with the text names that you created for each colour group, and a numeric value for those groups (which ioGAS uses in generating the plots). This can be exported as an excel or csv file for use in other applications.

## Slide 41
Ternary plots are useful because they are diagrams based on the ratios of 3 elements, and overcome any problems caused by “Closure”.
ioGAS has a tool for creating customized discrimination diagrams.
In this case study, select Nb-Sc-Th. Go to Diagrams, New Ternary Diagram.

## Slide 42
Add a new Polygon
Change Polygon name/colour
Save Diagram
Edit diagram name/labels
In this case study, select Nb-Sc-Th. Go to Diagrams, New Ternary Diagram. Add new polygons to enclose the defined groups. Give the polygons a name and colour. Save the diagram. Next time you start ioGAS this diagram will be available to automatically assign data to the defined compositions.

## Slide 43
Here is an example of a finished diagram.

## Slide 44
If you were starting the classification of the original data file from scratch, or intrepreting data from new drill holes completed on this project, you could apply the classification diagram. Open the diagram xml file.

## Slide 45
Colour rows by polygon
This does an automatic classification with a single click.

## Slide 46
An important next step beyond classifying the data is to understand what those groups mean. We can start by comparing with a library of rock compositions within ioGAS. On the right hand tool ribbon, click on the Mineral and Rock Nodes setting icon. Go to the rocks tab, USGS (silicate). Select a suite of rock compositions, including a basalt, andesite, rhyolite, etc. Then click on the Show Mineral and Rock Nodes icon.

## Slide 47
The Show Mineral and Rock Nodes icon function overlays the selected rock or mineral compositions on your geochemistry plots. If you are interpreting geochemical analyses, it is VERY helpful to ubderstand the expected trace element abundances in each rock type. The rock nodes in ioGAS are not great. A better general refence is contained within the AusIMM Monograph 9: Field Geologists Manual.

## Slide 48
Consider the compositions of the mafic rocks. The major element contents classify these rocks as mafics (see the Jensen Cation Plot). However these rocks have high abundances of high field strength elements (Nb, Th, Ce, possibly Zr and especially P), but very low Sc compared to typical basalts. The V/Sc plot of the workshop data on the left is compared to an Archean data set on the right, with tholeiitic ilmenite-series basalts. The mafic rocks in the Workshop data are depleted in Sc, but have a higher V/Sc ratio. These are alkalic magmas that have fractionated a significant volume of pyroxene; they are oxidized magmas hence Fe-silicate fractionation removed Sc at a faster rate than V. This is unusual in pyroxene-bearing rocks. It indicates an anomalously oxidized mantle source.
Alkalic magmas typically have high Ti, Nb, P, Th, REE’s. This could be a result of a low degree of partial melting and/or fractionation.
Ilmenite-series basalt plots in here

## Slide 49
Magmas associated with porphyry Cu deposits typically have low abundances of all the high field strength elements. The hornblende biotite porphyry in this workshop is a very typical example; Ti 1000 to 4000ppm, Nb 2 to 6ppm, Y 5 to 10ppm, Th 2 to 4ppm, Ce 20 to 50ppm. This is because porphyry Cu magmas typically fractionate titanite, and titanite is a great host mineral for these elements.

## Slide 50
The rhyolite groups in yellow and blue have higher abundances of high field strength elements because without a suitable host mineral, these elements are incompatible, ie they stay in the melt until late stages of crystallization.

## Slide 51
Olson, N.H., Dilles, J.H., Kent, A.J. and Lang, J.R., 2017. Geochemistry of the Cretaceous Kaskanak batholith and genesis of the Pebble porphyry Cu-Au-Mo deposit, southwest Alaska. American Mineralogist: Journal of Earth and Planetary Materials, 102(8), pp.1597-1621.
Mineral Chemistry from Pebble, Alaska
Representative REE and HFSE contents of titanite, zircon, and wholerock normalized to chondrite. Chondrite values from McDonough and Sun (1995). Fractionation of titanite accounts for the compatibility of Nb, Ta, REE’s, Th, Zr, Hf
Why are Porphyry Cu magmas depleted in Yttrium?
Garnet or Titanite fractionation?
Notes: This is a plot from Nansen Olsen from the Pebble PC system. It shows analyses of REE’s and HFSE’s in titanite (black traces) and zircons (grey traces) compared with average whole rock values (dashed lines). Note that the REE’s and Y, Nb, Ta, Th and U are 100 to 500 times more abundant in titanite than in the whole rock, with slightly lower factors for Zr and Hf. The difference between the titanite and WR values effectively provided a distribution coefficient between titanite and melt for these elements. Fractional crystallization of titanite would have a very significant impact on the WR values for these elements.

## Slide 52
Olson, N.H., Dilles, J.H., Kent, A.J. and Lang, J.R., 2017. Geochemistry of the Cretaceous Kaskanak batholith and genesis of the Pebble porphyry Cu-Au-Mo deposit, southwest Alaska. American Mineralogist: Journal of Earth and Planetary Materials, 102(8), pp.1597-1621.
Median values for trace elements in Titanite vs Whole Rock
Titanite; CaTiSiO5, 24 weight% Ti.
If ALL of the WR Ti was in titanite, these rocks would have 1.2% titanite. (there is also Ti in hornblende and magnetite)
Titanite accounts for almost all the WR budget of the REE’s and HFSE’s
Removing 50% of titanite by fractional crystallization halves the REE’s and HFSE
Why are Porphyry Cu magmas depleted in Yttrium?

## Slide 53
Zircon mineral chemistry has been a hot research topic in the last decade. Some of the Zr story can be inferred from whole rock chemistry. Most of the Zirconium and Hafnium is hosted in zircons. The plot on the left is a database of around 50,000 WR analyses. The Zr/Hf ratio is tightly clustered around 36:1. The plot on the right is from the Pebble porphyry Cu deposit. The low ratio in the leucocratic granite porphyry is due to fractional crystallization of zircons; otherwise the WR values still cluster around 36.
Olson, N.H., Dilles, J.H., Kent, A.J. and Lang, J.R., 2017. Geochemistry of the Cretaceous Kaskanak batholith and genesis of the Pebble porphyry Cu-Au-Mo deposit, southwest Alaska. American Mineralogist: Journal of Earth and Planetary Materials, 102(8), pp.1597-1621.

## Slide 54
These are whole rock analyses from the Pebble porphyry Cu deposit. The low ratio in the leucocratic granite porphyry is due to fractional crystallization of zircons; otherwise the WR values still cluster around 36.
Olson, N.H., Dilles, J.H., Kent, A.J. and Lang, J.R., 2017. Geochemistry of the Cretaceous Kaskanak batholith and genesis of the Pebble porphyry Cu-Au-Mo deposit, southwest Alaska. American Mineralogist: Journal of Earth and Planetary Materials, 102(8), pp.1597-1621.
Pebble intrusives
WR Zr:Hf averages 35 to 40

## Slide 55
These are LA-ICP-MS analyses of titanite and zircon grains from Pebble. If all of the Hf was contained in zircons, and the WR Zr:Hf ratio was 36:1, then the Hf content of zircons should be 13,800ppm. However the Hf values vary from 7,000 to 15,000ppm, with higher Hf in more fractionated intrusions. There must be another mineral that is preferentially taking in Hf. That mineral is titanite. Titanite has a typical Zr:Hf ratio of around 13:1. Partitioning of Hf between titanite and zircons leads to zircons having significantly higher Zr:Hf than the WR ratio.
With increasing fractionation in porphyry Cu magmas, titanite (with Ti, Nb and Hf) is removed and the Hf content of zircons increases in more evolved melts.
Olson, N.H., Dilles, J.H., Kent, A.J. and Lang, J.R., 2017. Geochemistry of the Cretaceous Kaskanak batholith and genesis of the Pebble porphyry Cu-Au-Mo deposit, southwest Alaska. American Mineralogist: Journal of Earth and Planetary Materials, 102(8), pp.1597-1621.
WR Zr:Hf = 36

## Slide 56
The liquidus temperature of plagioclase is highly dependent on pressure and water content. At high pressure and high water, plagioclase crystallization is suppressed, especially the sodic end of the solid solution. Without fractionation of sodic plagioclase, Na and Sr are retained in the melt to lower temperatures than they would be in mid-crustal (low pressure) melts. The Sr/Y ratio shows the combined effect of titanite fractionation and plagioclase suppression. Note the relative positions of the red versus yellow/blue groups.
This diagram is only useful where hydrothermal alteration has NOT removed Sr.

## Slide 57
Normally I would only use this diagram to track alteration, but in this case, there has not been a high degree of alkali metasomatism.
The porphyry magmas have not fractionated sodic plagioclase, so the final solidified porphyries end up with more albite than K feldspar. This is completely typical of porphyry Cu systems. In contrast, the low pressure mid-crustal melts have fractionated plagioclase extensively and have evolved to much more potassic compositions.

## Slide 58
The effect of plagioclase fractionation, or lack of, can also be seen in the aluminium contents.
Porphyry Cu magmas typically have high aluminium, while felsic magmas that have extensively fractionated plagioclase tend to have significantly lower Al.

## Slide 59
Something else that is very useful in ioGAS is to create a customized Rock Node table from your data. To do this, start by selecting all aliased variables. Then go to Analysis, Summary Stats.

## Slide 60
On the right hand tool ribbon, there is an icon that leads to a menu where you can choose which stats to display. Turn on just the median values.

## Slide 61
Again on the right hand tool ribbon, these median values can be exported as a csv file.

## Slide 62
Open the csv file and edit it. Add 4 columns named Group, Name, Description, Short name, as shown below.

## Slide 63
Open the spreadsheet of median values into a new ioGAS project. Select all aliased variables. On the top tool ribbon, go to File, User Nodes.
Assign the column names. Save the file.

## Slide 64
Next time you open an ioGAS project, the spreadsheet of median assay values from the rock units in the workshop data will be available to select as a Minerals and Rock Nodes overlay.

## Slide 66
Preparing Plots for presentations
To add any plot to a powerpoint presentation or document, click on the header bar of the plot to make this the active screen, and then Copy Window.

## Slide 67
Preparing Plots for presentations
If you use a right mouse click on the plot before you copy and paste, it opens a dialogue box which you can use to change the title, labels on axes, and ranges on axes. If you click on Windows Settings, you can change the font size.

## Slide 68
Preparing Plots for presentations
Al alternative to editing labels and fonts within ioGAS is to right click, Save, Save SVG, then paste this into powerpoint.

## Slide 69
Preparing Plots for presentations
If you use the Ungroup tool on the svg file in Powerpoint, every part of this can be edited.
Better still, these files can be imported into Adobe Illustrator and edited to a standard suitable for publication.

## Slide 70
Preparing Plots for presentations
Click on the Legend icon in the top tool ribbon. Right click on the actual legend, Copy, Copy(SVG). Then paste into powerpoint. Use the Ungroup tool (there are nested group layers). Once everything is ungouped, every part of the legend can be edited with suitable titles, text, font etc.

## Slide 71
Data
Cross Validation
Interpretation
Knowledge